## Slide 1: Biomedical Laboratory – 4th Year
Detecting a Cell Using Image Segmentation
Part : one
Image Processing Using MATLAB
Lab. No.“1”

## Slide 2
Introduction
Introduction
An object can be easily detected in an image if the object has sufficient contrast from the background of the image.
Step 1: Read and Display the Image
Step 2: Detect Entire Cell
Step 3: Dilate the Image
Step 4: Fill Interior Gaps
Step 5: Remove Connected Objects on Border
Step 6: Smoothen the Object
Step 7: Outline Creation
Procedural steps:
Application:
Edge detection and basic morphology tools are used to detect a prostate cancer cell.
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 3
Step 1: Read and Display The Image
Read The Image
I = imread('filename.fmt') :reads a grayscale or color image specified by filename and format fmt and stores it into array variable I. If the file is not in the current folder, or in a folder on the MATLAB path, specify the full pathname as:
I = imread(‘D:\pictures\asd.jpg’)
1.1 Key Commands:
figure :creates a new figure object using default property values, and automatically becomes the current figure until a new figure is either created or called.
imshow(I) :displays the stored image of the variable array I.
title('string') :adds the title specified by ‘string’ at the top and in the center of the current axes or figure.
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 4
Step 1: Read and Display The Image
Read The Image
I = imread('cell.tif');
figure, imshow(I), title('original image');
Read in the 'cell.tif' image, which is an image of a prostate cancer cell.
1.2 Step application:
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 5
Step 2: Detect Entire Cell
Detect Entire Cell
Two cells are present in that image, but only one cell can be seen in its entirety. We will detect this cell.
Another word for object detection is segmentation.
The object to be segmented differs greatly in contrast from the background image.
Changes in contrast can be detected by operators that calculate the gradient of an image.
The gradient image can be calculated and a threshold can be applied to create a binary mask containing the segmented cell.
First, we use edge and the Sobel operator to calculate the threshold value. We then tune the threshold value and use edge again to obtain a binary mask that contains the segmented cell.
2.1 Preface:
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 6
Step 2: Detect Entire Cell
Detect Entire Cell
2.2 Key Commands:
[BW threshold]= edge(I,'sobel') :returns threshold value for the Sobel method.
Hint:
That can be replaced by:
BW = edge(I,'sobel',(graythresh(I)*0.5));
BW = edge(I,'sobel',threshold*factor) :specifies the sensitivity threshold for the Sobel method. edge ignores all edges that are not stronger than threshold*factor. If you do not specify threshold*factor, or it is empty ([]), edge chooses the value automatically.
Question:
What are the other methods supported by edge function?
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 7
[BW threshold] = edge(I, 'sobel');
Factor = 0.1;
BWs = edge(I,'sobel', threshold * Factor);
figure,imshow(BWs),title('binary gradient mask');
2.3 Step application:
Detect Entire Cell
Step 2: Detect Entire Cell
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 8
Step 3: Dilate the Image
Dilate the Image
The binary gradient mask shows lines of high contrast in the image. These lines do not quite delineate the outline of the object of interest.
Compared to the original image, you can see gaps in the lines surrounding the object in the gradient mask.
These linear gaps will disappear if the Sobel image is dilated using linear structuring elements, which we can create with the strel function.
3.1 Preface:
3.2 Key Commands:
BWsdil = imdilate(BWs,SE) :dilates the grayscale, binary image BWs to the dilated image BWsdil. The argument SE is a structuring element object, or array of structuring element objects, returned by the strel function.
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 9
Step 3: Dilate the Image
Dilate the Image
SE = strel('line', LEN, DEG) creates a flat symmetric linear structuring element. DEG is the angle (in degrees) in a counterclockwise direction from the horizontal axis. LEN is the length of the line.
SE = strel(shape, parameters) :creates a structuring element, SE, of the type specified by shape as ‘line’, ‘square’, ‘diamond’, ‘disk’, ‘octagon’, ‘rectangle’, …etc. Depending on shape, strel can take additional parameters as:
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 10
SE = strel('square', W) :creates a square structuring element whose width is W pixels. W must be a nonnegative integer scalar.
Step 3: Dilate the Image
Dilate the Image
SE = strel('diamond', R) :creates a diamond-shaped structuring element, where R specifies the distance from the origin to the points of the diamond. R must be a nonnegative integer scalar.
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 11
se90 = strel('line', 3, 90);
se0 = strel('line', 3, 0);
BWsdil = imdilate(BWs, [se90 se0]);
figure, imshow(BWsdil);
title('dilated gradient mask');
3.3 Step application:
Step 3: Dilate the Image
The binary gradient mask is dilated using vertical structuring element followed by horizontal structuring element:
Dilate the Image
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 12
Step 4: Fill Interior Gaps
Fill Interior Gaps
The dilated gradient mask shows the outline of the cell quite nicely, but there are still holes in the interior of the cell. To fill these holes we use the imfill function.
4.1 Preface:
4.2 Key Commands:
BWdfill = imfill(BWsdil,'holes') :fills holes in the binary image BWsdil. A hole is a set of background pixels that cannot be reached by filling in the background from the edge of the image.
Hint:
'holes': are defined as an area of dark pixels (Black) surrounded by lighter pixels (White).
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 13
BWdfill = imfill(BWsdil, 'holes');
figure, imshow(BWdfill);
title('binary image with filled holes');
4.3 Step application:
Fill Interior Gaps
Step 4: Fill Interior Gaps
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 14
Step 5: Remove Connected Objects on Border
Remove Connected Ojects on Border
The cell of interest has been successfully segmented, but it is not the only object that has been found.
Any objects that are connected to the border of the image can be removed using the imclearborder function.
The connectivity in the imclearborder function was set to 4 to remove diagonal connections.
5.1 Preface:
5.2 Key Commands:
Bwnobord = imclearborder(BWdfill,conn) :suppresses structures that are lighter than their surroundings and connected to the image border (clear the image border) with the desired connectivity conn. The connectivity may be 4 or 8 for two dimensions.
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 15
Step 5: Remove Connected Objects on Border
Remove Connected Ojects on Border
connectivity of white pixels = 4
connectivity of white pixels = 8
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 16
BWnobord = imclearborder(BWdfill, 4);
figure, imshow(BWnobord);
title('cleared border image');
5.3 Step application:
Step 5: Remove Connected Objects on Border
Remove Connected Ojects on Border
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 17
Step 6: Smoothen the Object
Smoothen the Oject
In order to make the segmented object look natural, we smoothen the object by eroding the image twice with a diamond structuring element. We create the diamond structuring element using the strel function.
6.1 Preface:
6.2 Key Commands:
BWfinal = imerode(BWnobord,SE) :erodes the grayscale binary image BWnobord, returning the eroded image BWfinal. The argument SE is a structuring element object or array of structuring element objects returned by the strel function.
Eroding process to smoothen the objected is required as consequences of dilation process of the object.
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 18
seD = strel('diamond',1);
BWfinal = imerode(BWnobord,seD);
BWfinal = imerode(BWfinal,seD);
figure, imshow(BWfinal);
title('segmented image');
6.3 Step application:
Smoothen the Oject
Step 6: Smoothen the Object
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 19
Step 7: Outline Creation
Outline Creation
Finally, the method of displaying the segmented object would be to place an outline around the segmented cell. The outline is created by the bwperim function.
7.1 Preface:
7.2 Key Commands:
BWoutline = bwperim(BWfinal) :returns a binary image containing only the perimeter pixels of objects in the input image BWfinal. A pixel is part of the perimeter if it is nonzero and it is connected to at least one zero-valued pixel.
Outline is created on a copy of the original intensity image depending on the perimeter pixels of object with lighten pixels (white = 255)
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 20
BWoutline = bwperim(BWfinal);
Segout = I;
Segout(BWoutline) = 255;
figure, imshow(Segout);
title('outlined original image');
7.3 Step application:
Outline Creation
Step 7: Outline Creation
Notes: Analytical model is derived based on governing physical laws for the system such as Newton's law, Ohms law, etc.
Experimental model is derived based on experimental empirical results and samples for the system.
Numerical values of the model parameters are often approximated from experimental data by curve fitting.
Discrimination learning models are drived

## Slide 21
Questions and Discussion
Questions and Discussion